AHD MOBILE DVR

Hardware User Manual

(MR9604)

Catalogue

Chapter 1 Accessories and Interface	1

1．MDVR and accessories	1

2．System connection	3

3．Panel introduction	4

4．Interfaces Definition	4

4.1 Power interface	4

4.2 I/O Interface definition	5

4.3 Aviation interface definition	5

Chapter 2 Installation and Application	6

1. SD card installation	6

2. Antennas Connection	6

3. Power Connection	7

4. Camera Connection	7

5. Monitor connection	8

6. Intercom connection	9

7. I/O wires connection	9

7.1 IR extension connection	9

7.2 Alarm input connection	10

7.2.1 Application of Alarm input (Reverse assistant)	10

7.2.2 Application of Alarm Input (Emergency Alarm)	12

7.3 Serial ports connection	13

7.3.1 TTS connection	13

7.3.2 Fuel sensor connection	14

Chapter 1 Accessories and Interface

1．MDVR and accessories

Before you use this product please check the accessories in the packing box. If there is anything missing or damaged please contact your seller. The MDVR and accessories are listed as following:

List of MDVR and accessories

| Description | Picture | Quantity |
| --- | --- | --- |
| MDVR |  | 1 |
| Power cable |  | 1 |
| I/O cable |  | 1 |
| AV cable |  | 1 |
| GPS antenna (Optional) |  | 1 |
| WiFi antenna (Optional) |  | 1 |
| 3G/4G antenna (Optional) |  | 1 |
| Remote control (Optional) |  | 1 |
| IR Extension cable (Optional) |  | 1 |
| Mouse (Optional) |  | 1 |
| Intercom (Optional) |  | 1 |

- System connection

System connection

3．Panel introduction

Front panel

Back panel

4．Interfaces Definition

Here we introduce the definition of the interfaces of Power, I/O, AV Input & Output. See as following:

4.1 Power interface

Power interface definition

4.2 I/O Interface definition

Front view of I/O Interface

I/O Interface definition

| PIN | Color | Definition | PIN | Color | Definition |
| --- | --- | --- | --- | --- | --- |
| 1 | Grey | IR_IN | 2 | Red | PWR_5V |
| 3 | Purple | Alarm IN1_NEG | 4 | Brown | Alarm_OUT |
| 5 | Purple | Alarm IN3_NEG | 6 | White | TXD 1 |
| 7 | Purple | Alarm IN2_POS | 8 | Yellow | RXD 1 |
| 9 | Purple | Alarm IN4_POS | 10 | Blue | TXD 2 |
| 11 | Black | GND | 12 | Green | RXD 2 |

4.3 Aviation interface definition

AV-IN Camera Interface                   AV-OUT Monitor Interface

Chapter 2 Installation and Application

1. SD card installation

Please insert the key into the hole of the lock on the front panel, and switch it to be open status, then pull the cover toward right, you will see the SIM and SD card slots.

SD card Installation

Please insert the SD card into the slot as per the icon indication, Then close the SD cover and lock it (Please remember to lock it, otherwise, The SD card and 3G/4G will not work)

SD card installation

2. Antennas Connection

Please connect the WiFi, 3G/4G and GPS antennas as per the picture as followed. We suggest you put the GPS antenna externally at the vehicle’s roof to make sure signal connection even when it is weak.

Antennas Connection

3. Power Connection

Please connect the power as per the definition of power interface. Positive pole (RED) connects with power input 9-36V DC, ACC ignition (YELLOW) connects with 5-36V DC.

Power Connection

The yellow ignition wire is used to detect the ignition signal. We strongly suggest you connect it with the “RUN” terminal of the ignition switch, or any terminal in the vehicle’s switch box which will have power only when the vehicle was ignited (f.g. the FM radio)

PS: When testing the device, please connect both of the red power wire and the yellow ignition wire with the positive pole of the UPS, otherwise, the device will not boot.

4. Camera Connection

You can connect the camera with the AV input cable directly, or by extension cable (optional). The AV cable in the accessories box has mark on each connector, AV 1-4 are for cameras connection.

Cameras Connection

PS: Before you connecting the cameras, please double check the definition of the AV interface, please make sure your cameras are with same aviation interface definition with the DVR.

5. Monitor connection

The device supports VGA and CVBS output. You can switch the output mode to be the one you need by the mouse or remote control.

Aviation interface monitor connection

PS: Before you connecting the monitor, please double check the definition of the AV interface, please make sure your monitor is with same aviation interface definition with the DVR.

6. Intercom connection

When you’re going to use the intercom, please connect the cables which come with the intercom. If the cable is not long enough for you, you can use extension cable.

Intercom Connection

PS: The intercom cable only comes with the intercom, they are one set.

7. I/O wires connection

When you're going to use it, please connect the wires as the I/O interface definition. You will also find tips of the interface definition in the DVR menu.

7.1 IR extension connection

IR extension connection

| I/O wires |  | IR extension cable |
| --- | --- | --- |
| PIN | Definition | Color |  | Color | Definition |
| 11 | Ground | Black |  | Black | Ground |
| 2 | 5V Output | Red |  | Red | 5V Power |
| 1 | IR extension | Grey |  | White | Signal |

IR Connection

7.2 Alarm input connection

This device provides 4 channels alarm inputs (2 channels Positive trigger, 2 channels negative trigger). You can connect the positive pole of circuit of the reverse light, turn light, door open & close etc with them for applications such as reverse assistant, camera channels switching. You can also connect it with the SOS emergency button for alarm linkage.

Alarm Input Connection

| I/O wires |  | Alarm Trigger |
| --- | --- | --- |
| PIN | Definition | Color |  | Color | Alarm trigger |
| 3 | Alarm input1 | Purple |  | Red | Ground |
| 5 | Alarm input3 | Purple |  |  |  |
| 7 | Alarm input2 | Purple |  | Black | 5-32V |
| 9 | Alarm input4 | Purple |  |  |  |

Alarm Input Connection

7.2.1 Application of Alarm input (Reverse assistant)

The device comes with Reverse assistant feature, give an example with Alarm Input2, we connect the wire of alarm input 2 with the positive pole of reverse light’s power, see as following:

Reverse Assistance Connection

| I/O wires |  | Alarm trigger |
| --- | --- | --- |
| PIN | Definition | Color |  | Color | Alarm Trigger |
| 7 | Alarm input 2 | Purple |  | Red | Positive pole of Reverse light |

Reverse Assistance Connection

Setup it in the DVR menu “Advanced”   “RearCamera”, see as following, click “OK” to save your setting.

AV: Please select the reverse camera’s channel

InputSwitch: Please select the alarm input number which connect with the reverse light’s power

PS: When using reverse assistance, please use IN2, IN4 positive trigger to setup

When you put reverse gear, the DVR will display the reverse camera’s channel only. See as following:

Reverse Assistance

7.2.2 Application of Alarm Input (Emergency Alarm)

You can connect an Emergency Button With the alarm input of the device. When you hit the Emergency alarm button, the device will send alarm information to the server platform. That is alarm linkage. (This application requests the DVR connecting with the server in real time, otherwise, the server platform will not receive the alarm information). We give an example with Alarm Input 1, connect the I/O alarm input wire 1 with one terminal of the Emergency button, and connect the other terminal of the Emergency button with ground.

Emergency button connection

| I/O wires |  | Alarm trigger |
| --- | --- | --- |
| PIN | Definition | Color |  | Color | Alarm trigger |
| 3 | Alarm input1 | Purple |  | Red | Ground |

Emergency button connection

PS: (If the connected Alarm input is Positive trigger, the other end of the Emergency button will be 5-32V DC power)

Setup it in the DVR menu “Alarm”    “Input”, select AlarmInput1 in the list to setup the alarm parameter. See as following:

Setup alarm input

ChnInput: This channel is used to connect with the Emergency button.

UploadType: When you use the emergency button, please set up it to be “Urgency”, otherwise, set up it to be “No”

7.3 Serial ports connection

The device provides 2*RS232 ports, UART0 is for TTS and fuel sensor, UART1 is for SerialNet (Pass Through)

7.3.1 TTS connection

Pick out the wire of RS232 UART0 as per the PIN definition of I/O interface and connect it with the TTS device as following:

TTS Connection

| I/O wires |  | TTS wires |
| --- | --- | --- |
| PIN | Definition | Color |  | Color | Definition |
| 2 | 5V output | Red |  | Red | 5V input |
| 6 | TXD 1 | White |  | Green | RXD |
| 8 | RXD 1 | Yellow |  | Yellow | TXD |
| 11 | Ground | Black |  | Black | Ground |

TTS Connection

Path of setup in the menu: Advance->UART->UAR”0, Select “TTS” in “Function”

TTS setup

7.3.2 Fuel sensor connection

Pick out the wire of RS232 UART0 as per the PIN definition of I/O interface and connect the fuel sensor as following. The fuel sensor works with 9-36V, the DVR cannot power on it.

Fuel sensor connection

| I/O wires |  | Fuel sensor connection |
| --- | --- | --- |
| PIN | Definition | Color |  | Color | Definition |
| / | / | / |  | Red | External power input 9V-36V |
| / | / | / |  | Black | Ground of External power |
| 6 | TXD 1 | White |  | Blue | RXD |
| 8 | RXD 1 | Yellow |  | Yellow | TXD |
| 11 | Ground | Black |  | Brown | Ground |

Fuel sensor connection

Path of setup in the menu: Advance->UART->UAR”0, select “Fuel” in “Function”

Fuel sensor setup

# Text boxes

ggps

Negative trigger: Ground

Positive trigger interface: IN2, IN4

Negative trigger interface: IN1, IN3

Positive trigger: 5-32V

Adjust the lines by dragging the blue points

Click “Zone”