|  | 4ch AHD DUAL SD MOBILE DVR MR9604 |
| --- | --- |

FEATURES:

Built-in high performance Hisilicon chipsets, coded with H.264 standard, high compression rate and image qulity 4CH AV Inputs with AHD 720P/960H/D1/CIF optional, 1CH synchronized AV output, 1CH VGA output 4CH local recording with 720P resolution in real time Power: Professional In-Vehicle power design, 9-36V DC Wide Voltage Range Multi protection circuits like under-voltage, short, reversed plug-in Smart power management system, shutdown under low voltage, low consumption when standby Support 5V DC power output for cameras, LCD monitor etc Data Storage: Special file management system to encrypt and protect the data Proprietary technology to detect the bad track of the SD card which can make sure the continuity of video and long service life of the SD card Built-in ultracapacitor, avoid data loss and sd card damage caused by sudden outage Support dual SD card storage, maximum 256G each With M.2 interface for built-in SSD, maximum 256G Transmission Interface: Support 3G/4G transmission, LTE/HSUPA/HSDPA/WCDMA/EVDO/TD-SCDMA Support GPS/BD optional, high sensitivity, fast positioning Support wireless download by WiFi, 802.11b/g/n, 2.4GHz Built-in G-sensor to detect the driver’s driving habits

| Technical parameter: |
| --- |
| Item | Device parameter | Performance |
| System | Main processor | Hi3520DV200 |
|  | Operating system | Embedded Linux OS |
|  | Operating language | Chinese/English |
|  | Operating interface | GUI, support mouse |
|  | Password security | User password/Admin password |
| Video | Video standard | PAL/NTSC |
|  | Video compression | H.264（Main Profile） |
|  | Image resolution | 720P /960H/D1/CIF |
|  | Playback quality | 720P /960H/D1/CIF |
|  | Compound mode | 4ch 720P/4ch 960H/2ch 720P+2ch 960H |
|  | Decoding ability | 1ch 720P real time |
|  | Video input | 4ch video input, aviation interface |
|  | Video output | 2ch video output (1ch video output, 1ch VGA) |
|  | Recording quality | Class 1-6 optional |
|  | Image display | Single/QUAD display optional |
| Audio | Audio compression | G.726 |
|  | Audio input | 4ch audio input, aviation interface |
|  | Audio output | 1ch audio output, aviation interface |
|  | Audio recording | Audio & Video synchronized recording |
| Recording & Playback | Recording mode | Manual/Alarm |
|  | Video bit rate | Full frame 4096Mbps，6 classes image quality optional |
|  | Audio bit rate | 8KB/s |
|  | Storage media | 2 SD card and 1 SSD with M.2 interface |
|  | Video inquiry | Inquiry by channel/recording type |
|  | Local playback | Playback by file |
| Firmware upgrading | Upgrading mode | Manual/Automatical/Remote |
|  | Upgrading method | USB disk/Wireless network |
| Interface | Video input | 4ch aviation interface |
|  | Video output | 1ch aviation interface, 1ch VGA |
|  | Audio input | 4ch aviation interface |
|  | Audio output | 1ch aviation interface |
|  | Alarm input | 4 digital inputs (2 positive trigger, 2 negative trigger) |
|  | Alarm output | 1 output (currenct<150mA, with built-in resettable over-current protector) |
|  | SD card | 2 SDXC high speed card (up to 256G each) |
|  | SSD interface | With M.2 interface for built-in SSD (up to 256G) |
|  | USB interface | 1 USB 2.0 (support U disk/mouse) |
|  | Ignition input | 1 ACC signal |
|  | RS232 interface | 2* RS232 |
|  | IR interface | 1 built-in IR receiver |
|  | LED indication | PWR/RUN/DISK/CELL/WIFI/GPS |
|  | SD card lock | 1 |
|  | Debug port | 1 |
| Function extension | GPS | Support detecting antenna plug in/Unplug/Short circuit |
|  | 3G/4G | LTE/HSUPA/HSDPA/WCDMA/EVDO/TD-SCDMA |
|  | WIFI | 802.11b/g/n, 2.4GHz |
|  | G-SENSOR | Support motion detecting Support driving habits detecting (heavy acceleration/hard braking/sharp turns/crash) |
| Others | Power input | 9~36V DC（ISO7637 P5A 200V） |
|  | Power output | 5V 300mA |
|  | Power consumption | Standby 3mA Maximum consumption 18W @12V 1.5A @24V 0.75A |
|  | Working temperature | -20---70℃ |
|  | Storage | 720P 1G/h/channel 960H 750M/h/channel |
|  | Dimension | 165*142*45 mm |

Front Panel:

Back Panel: